## Slide 1: Dhubri - Phulbari Bridge: Genesis of Bridge Form
Neil Banerjee

## Slide 2: Project Details
This bridge is connecting Dhubri town in Assam & Phulbari town in Meghalaya.
The bridge is a part of NH-127B.
Four lane bridge having main navigational span of 12.625km with viaduct of 5.735 km.
Reduction of Travel time by 6 hours & travel distance from 210km to 20km.

## Slide 3: Navigational Requirements (IWAI guidelines)
10 meter vertical clearance above High Flood Level (HFL)
100 meter horizontal clearance between piers
Pictures of Brahmaputra River at Bridge Location

## Slide 4: Option - 1: Through Type Truss Bridge for Navigational Span
Span Arrangement | Single span arrangement
Cost (Approx.) | ₹ 37,500 Million
Construction Time (Approx.) | 8 years
FRL
Cross Section of Bridge Option

## Slide 5: Option - 2: Bowstring Arch Bridge for Navigational Span
Span Arrangement | Single span arrangement
Cost (Approx.) | ₹ 99,500 Million
Construction Time (Approx.) | 6.5 years
Cross Section of Bridge Option
FRL
Similar Bridge Form: Sydney Harbour Bridge

## Slide 6: Option - 3: Cable Stayed Bridge for Navigational Span
FRL
100m
50m
25m
125m
Span Arrangement | Single span arrangement
Cost (Approx.) | ₹ 1,60,000 Million
Construction Time (Approx.) | 6.5 years
Cross Section of Bridge Option
Similar Bridge Form: Charles W. Cullen Bridge

## Slide 7: Option - 4: Segmental Balanced Cantilever Bridge for Navigational Span
FRL
FRL
Span Arrangement | 4 Span continuous
Cost (Approx.) | ₹ 23,000 Million
Construction Time (Approx.) | 7.5 years
Similar Bridge Form: Sir Leo Hielscher Bridge
Cross Section of Bridge Option

## Slide 8: Option - 5: Extradosed Bridge for Navigational Span
FRL
Span Arrangement | 4 Span continuous
Cost (Approx.) | ₹ 22,500 Million
Construction Time (Approx.) | 7.5 years
Cross Section of Bridge Option
Similar Bridge Form: Pearl Harbor Memorial
Bridge

## Slide 9: Decision Matrix
Sl No | Bridge Type | Cost | Construction Time | Maintenance | Aesthetic | Complexity of Construction
1 | Truss Bridge | High | Moderate | High | Moderate | Moderate
2 | Bowstring Arch Bridge | High | Moderate | High | Moderate | Complex
3 | Cable Stayed Bridge | High | Moderate | Moderate | Excellent | Complex
4 | Segmental Balanced Cantilever Bridge | Economic | Moderate | Low | Poor | Easy
5 | Extradosed Bridge | Most Economic | Moderate | Moderate | Excellent | Moderate

## Slide 10: Conclusion
As per the above study, an Extradosed bridge option is proposed based on the following points:
Aesthetics
Engineering Aspects
  Flexible structure preferable in high seismic zone
  Low fatigue than Cable stayed bridge etc.
Accessibility during Construction
Serviceability & adaptation to future requirements
  Can increase the load carrying capacity
Cost of Construction

## Slide 11: Animated View of Dhubri - Phulbari Bridge